Message Signalled Interrupts in Mixed-Master Control
Wesley W. Terpstra
GSI, Germany
ICALEPCS 2015

---
What is FAIR?

---
Where is the ring?

---
What controls it?

---
What is inside it?
FPGA
This talk: the links between cores

---
What is Wishbone?
Wishbone: synchronous parallel bus
Simple master-slave connections only

---
What is Wishbone?
Wishbone: synchronous parallel bus
Simple master-slave connections only
CYC
STB
STALL
ACK
Unstalled request

---
WB bus is extended using crossbars
A crossbar acts as a network switch
Slave ports for masters and master ports for slaves

---
Big systems have multiple crossbars
Our timing receivers contain ~50 WB components
Nesting crossbars is a useful organizational tool
Hot plugged
Works Great! (TM)

---
What's the problem?
In Wishbone, all communication initiated by master
Sometimes slaves must tell the master they have data
Help! I'm on fire!

---
Approach: Classic interrupts
Slaves connected to a predetermined master
Interrupt priorities fixed at design-time (shared line)
Master must query all slaves to find source
Cheap, but ... Not composable

---
Approach: Message Signalled (MSI)
Invert Wishbone bus
Slaves send messages to masters
Address selects master

---
Requirements for Using MSI
MSI-enabled masters provide
A slave link to the MSI bus
A range of addresses to receive MSIs
potentially with different priority queues
MSI-enabled slaves provide
A master link to the MSI bus
For each type of MSI message (burning / ready / full)
A register to select which address receives it
A register to enable the MSI

---
MSI is composable
Masters set address in slave's MSI target address register
Slaves can notify any master which controls them
Masters have thousands of “interrupt target addresses”
Can immediately distinguish source of MSI
Can prioritize MSIs by choosing destination queue
Composable: plug crossbars together

---
Addressing and SDB
To find slaves, masters recursively search SDB
Slaves addresses differ as seen from different masters
Addresses describe a path, not a destination

---
Addressing and SDB
In MSI bus, master address differs from slave PoV
When masters scan bus, also scan backwards path
address slaves need to send master MSI
constructed bottom-up

---
WB+MSI well suited for complex buses
Wishbone scales well, from 2- to 50-component systems
MSI expands bus composability to interrupts
SDB must be extended with master records

---
Questions?